## Slide 1
SARA · Smart Assistive Reading Aid
A Wearable Assistive Glass for Authenticating Bangladeshi Banknotes: Fusing Physical Security Features and Deep Learning for Visually Impaired Users
A bilingual (Bangla and English) smart glass that also reads printed Bangla and English text and detects everyday objects, offline on a Raspberry Pi 5
Supervisor:
Mohammad Shidujaman, PhD
Assistant Professor
Department of Computer Science & Engineering
Submitted By:
MD Abdun Fattah Lam (2220014)
Mukut Protim Memo (2020086)
Tanjila Hossain Tapti (2130561)
Notes: We present SARA, a smart glass for blind and low-vision people in Bangladesh. It reads Bangla and English text, names objects, recognises Taka notes and checks them carefully, and it works on the device without the internet. The photo is the current prototype.

## Slide 2: Introduction
At least 2.2 billion people have a near or distance vision impairment, and its prevalence in low- and middle-income regions is about four times that in high-income regions [1]
In Bangladesh, three everyday questions usually require help from another person:
  Money: which note was handed back, and is it genuine?
  Reading: what does a medicine label, sign or letter say?
  Surroundings: what or who is ahead?
In each case the blind person depends on an answer they cannot verify
SARA is an offline, bilingual assistive glass built for this setting
Money
Reading
Surroundings
Top row: today, an answer from another person. Bottom row: with SARA, the glass answers. (Illustration)
Notes: At least 2.2 billion people have a vision impairment, and it is about four times as common in low- and middle-income regions. In Bangladesh, three everyday questions usually need another person: which note was handed back and whether it is genuine, what a medicine label, sign or letter says, and what or who is ahead. In each case the blind person depends on an answer they cannot check. SARA is an offline, bilingual glass built for exactly this setting.

## Slide 3: Problem Statement
Visually impaired user
in Bangladesh
Money
Which note was handed back? Is it genuine?
Asks the shopkeeper
Reading
What does a medicine label, sign or letter say?
Asks family or a pharmacist
Surroundings
What or who is ahead?
Asks a stranger
An answer they cannot verify
A wrong note or a fake note can go unnoticed
A label or letter can be misread
Every task waits for someone else
Existing aids do not close this gap
OrCam MyEye [2]
Works offline, but Bangla is not among its listed languages; no Taka notes
Research glasses [3, 4]
Google Glass based systems and AIris send pictures to a server
Pi reading aids [5]
Low cost, but mostly English-only
Counterfeit-note studies [6, 7, 8, 9, 10]
Not brought to a wearable a blind user can operate
The gap
No reviewed device is offline, speaks Bangla and names Taka notes
Notes: This flowchart shows the problem. A visually impaired user has three everyday questions: money, reading and the surroundings. Each one is answered by another person, the shopkeeper, a family member or pharmacist, or a stranger, so the user ends up with an answer they cannot verify. Existing aids do not close this gap. OrCam MyEye works offline but does not list Bangla among its languages and does not name Taka notes. The research glasses send pictures to a server. Low-cost Raspberry Pi reading aids are mostly English-only. Studies on Bangladeshi counterfeit notes, and the JaalTaka benchmark, have not been brought to a wearable. So no reviewed device is offline, speaks Bangla and names Taka notes.

## Slide 4: Proposed Solution: SARA
Our prototype in a staged shop exchange: receiving a note, holding it up to the camera
Ask
Button press or voice: "Glass, check money" [11]
Capture
The glass camera takes a picture
Process offline
On the Raspberry Pi 5, no internet [12]
Taka recognition
Names the note [13]
Authenticity check
Watermark (DMWR) and UV security fibres
Text reading
Bangla and English [14, 15]
Objects and people
Names what is ahead [13, 16]
Safe verdict
"Likely genuine" or "check by hand"; it never says "counterfeit"
Spoken answer
Bangla or English speech [17] and a short vibration
পাঁচশত টাকার নোট "500 Taka note": the user knows without asking anyone
Offline: text, objects, Taka, emotion. Optional online: scene description only.
Notes: This flowchart is the same moment with SARA. The user presses a button or says glass, check money. The camera takes a picture, and the Raspberry Pi 5 processes it on the device without the internet. Depending on the mode, it recognises the Taka note, checks the watermark and the UV security fibres, reads Bangla or English text, or names objects and people ahead. For money, a safe verdict policy says likely genuine or check by hand, and never says counterfeit. The answer is spoken in Bangla or English with a short vibration, for example five hundred Taka note, so the user knows without asking anyone.

## Slide 5: System Features
Prototype version 2: the complete unit, the UV light on, the Pi 5 in the rear enclosure, buttons and power bank
Text reading
Bangla and English
Objects
Named in Bangla
Taka notes
Value + safe check
Emotion
Face in front
Online description
Optional; needs internet
How the user starts a mode: five buttons on the frame, or a voice command: "Glass, read text"
Models: text [14, 15] CRAFT + EasyOCR; objects [13, 16] YOLOv8 on COCO; emotion [18] RAF-DB; voice commands [11] Vosk.
Notes: This is the current prototype: the camera and five buttons sit on the frame, a bone-conduction earphone leaves the ears free, and the Raspberry Pi 5 rides in a ventilated enclosure at the back of the head. Five modes cover text, objects, Taka notes, emotion and an optional online description. Every mode can be started with a button or with a voice command that begins with the word glass.

## Slide 6: Research Questions
1
System
Can it all run on a Raspberry Pi 5?
2
Synthetic data
Can unlabelled training data detect real notes?
3
Number of views
Can one view of a note be enough?
4
Unseen prints
Does the check hold on new counterfeit prints?
5
Safety
Can it never accuse a genuine note?
6
Bangla OCR
What matters most for reading Bangla?
Notes: Six questions organise the talk. First, whether a multi-function Bangla glass runs on a Raspberry Pi 5 and how fast. Second, whether a Taka detector trained without hand labels works on real, hand-held photos. Third, why multi-view counterfeit models fail with fewer views and whether training fixes it. Fourth, how much accuracy drops on counterfeit prints never seen in training. Fifth, whether the glass can give counterfeit advice that never accuses a genuine note. Sixth, which part of a Bangla OCR pipeline matters most for a wearable camera.

## Slide 7: Literature Review: Existing Assistive Devices
OrCam MyEye [2]
Google Glass analysis [3]
AIris [4]
System | Reads Bangla | Knows Taka | Works offline | Wearable
OrCam MyEye [2] | No | No | Yes | Yes
Google Glass scene analysis [3] | No | No | No | Yes
AIris (2024) [4] | No | No | No | Yes
Raspberry Pi reading aids * | No | No | Partly | Partly
SARA (ours) | Yes | Yes | Yes | Yes
The research gap
None of the systems we reviewed combines Bangla, Taka and offline use.
Counterfeit tests reuse the same prints
Few report speed on the real device
Rows with a reference: from the cited source. * Our assessment of typical hobby builds, not a cited result.
Photos: OrCam MyEye by Ylip, CC BY-SA 4.0; Google Glass by Ted Eytan, CC BY-SA 2.0 (Wikimedia Commons); AIris from [4]. Comparison from [2, 3, 4].
Notes: Commercial glasses such as OrCam work offline but not in Bangla and not with Taka. Glass-based research systems send pictures to a server. Raspberry Pi reading aids are cheap but mostly English. No device combines Bangla, Taka and offline use, and counterfeit studies do not check for copies of the same print in training and test.

## Slide 8: System Architecture
Camera, buttons, voice
Camera 640×480
5 buttons on the frame
Voice: "glass, …"
Raspberry Pi 5
Mode manager
All models on the CPU
Offline, except the online mode
AI modules
Text: CRAFT + EasyOCR [14, 15]
Objects: YOLOv8s, COCO [13, 16]
Taka: YOLOv8s + safe checks
Emotion: YuNet + EfficientNet [18]
Online: cloud model (optional)
Audio + vibration
Bangla or English speech [17, 19]
Vibration for a note
Everything runs on the glass itself; only the optional online mode uses the internet.
Sources: [14] Baek et al. 2019; [15] EasyOCR; [13] Ultralytics YOLOv8; [16] COCO; [18] RAF-DB; [17] Piper; [19] eSpeak NG.
Notes: The camera picture, the buttons and voice commands go to a mode manager on the Raspberry Pi 5. The active mode runs its model on the CPU, and the result is spoken in Bangla or English, with a vibration for a detected note.

## Slide 9: Hardware Design
Raspberry Pi 5
4-core 2.4 GHz, 8 GB; runs every model [12]
Camera Module 2
8 MP IMX219, used at 640×480
Five push-buttons
MODE, ACTION, READ, VOL+, VOL−
Vibration motor
A buzz when a note is found
Bone-conduction headphone
Speech; the ears stay free
Power bank
USB-C supply for the Pi 5
Frame and UV lamp
3D-printed; UV-A 360–395 nm
Rear enclosure
Ventilated case for the Pi 5
Pictures (Wikimedia Commons): Raspberry Pi 5 by SimonWaldherr, CC BY 4.0; Camera Module v2 by the Raspberry Pi Foundation, CC BY-SA 4.0; vibration motor by Raimond Spekking, CC BY-SA 4.0; power bank by Pinguinguy, CC0. Buttons, headphone, frame and enclosure: our prototype.
Notes: The hardware of the second prototype. A Raspberry Pi 5 runs every model on its CPU. The Camera Module 2 is used at 640 by 480. Five push-buttons on the temple select and start the modes, a vibration motor confirms a found note, and a bone-conduction headphone speaks the result while leaving the ears free. A 3D-printed frame carries the camera and the UV-A lamp, and a ventilated enclosure at the back of the head carries the Pi. A power bank supplies it.

## Slide 10: Evolution of the Prototype
Version 1
Board on one temple
Front
Camera + UV lamp
Side
5 buttons, bone-conduction earphone
Rear
Pi 5 in a ventilated case
Version 2
Notes: The first version put the board and fan on one temple: heavy on one side and loud by the ear. Version two moves the Raspberry Pi into a ventilated enclosure at the back of the head, keeps the camera and a small UV lamp on the front, puts five buttons along the frame and uses a bone-conduction earphone so the ears stay free for traffic sounds.

## Slide 11: Banknote Detection: Synthetic Training Data
Note photos [20] are pasted onto real scenes [16], and the program writes every label itself.
SYNTHETIC COMPOSITES
0.995
mAP@0.5 on 2,282 held-out composites
REAL PHOTOS
94.1%
right note value on 1,536 photos taken by other people (laptop)
Sources: [20] BanglaTaka (Mendeley); [16] Lin et al., COCO, ECCV 2014; detector [13] Ultralytics YOLOv8. 94.1% with the hand-held detector (next slide).
Notes: Public Taka images are clean close-ups, so a model trained on them fails on a live camera. We pasted 5,073 note photos onto real COCO pictures with random angle, scale, light and blur, and let the program write the box labels. The detector scores 0.995 mAP on held-out composites and, the number that matters for users, names 94.1 percent of 1,536 real photographs taken by other people correctly. The two numbers measure different things: the first is on synthetic composites, the second on real photos.

## Slide 12: Banknote Detection: Hand-Held Notes
TRAINING: 6,000 SYNTHETIC CLOSE-UPS
TEST: REAL HAND-HELD PHOTOS
11.8% → 47.5%
Chart: Right note value, real hand-held photos (NSTU, 1,127)
| Laptop | Raspberry Pi (8-bit)
Earlier detector | 11.8 | 8.7
Hand-held detector | 47.5 | 33.5
Right note value on the laptop. Trade-off: with 3 notes in view, the total is right 97.0% (was 99.2%).
Sources: test photos [21] Rafi et al., NSTU-BDTAKA, Data in Brief 2024; detector [13] YOLOv8. Our results: paper_evidence/HANDHELD_FINETUNE.md.
Notes: A blind user holds the note close, folded and under the fingers, and our training pictures showed whole notes in scenes. We generated six thousand hand-held close-ups from training notes only and fine-tuned the detector. On the independent NSTU hand-held test, the right value rises from 11.8 to 47.5 percent on the laptop and from 8.7 to 33.5 percent on the Pi. There are costs: one-taka notes are named more often by mistake (36.6 percent), and with three notes in view the total is right 97.0 percent of the time instead of 99.2.

## Slide 13: Live Detection Tests
Informal demonstrations, not a measured accuracy study
Six note values (10 to 1,000 Taka) named at 0.63–0.89 confidence, including worn and folded notes. Laptop webcam and the first glass prototype.
Notes: These are live sessions with our own notes, with a laptop webcam and the first glass prototype. Ten, fifty, one hundred, two hundred, five hundred and one thousand Taka were named at 0.63 to 0.89 confidence, including worn and folded notes and two or three notes at once. Boxes are loose and can overlap when notes are close. These photos illustrate behaviour; we did not count an error rate in these sessions.

## Slide 14: Counterfeit Screening: Prefix-Robust Multi-View Training
Chart: Test accuracy by number of views (mean of 3 seeds)
| 1 | 2 | 3 | 4 | 5 | 6
Fixed six-view training | 71.2 | 73.1 | 85.7 | 90.5 | 90.5 | 98.1
Prefix training (ours) | 98.2 | 98.4 | 98.6 | 98.6 | 98.7 | 98.7
With a single view
71.2%
rises to
98.2%
Held-out JaalTaka test notes, never used for training or for any choice
Training on random first views: one view is enough.
Data: [9, 10] Piyas et al., JaalTaka dataset and article, 2025-2026 (1,390 notes, six views each; counterfeits seized by the Rapid Action Battalion).
Notes: A blind user cannot promise to capture six views of a note. A model trained only with all six views collapses to 71 percent with one view. Training on random prefixes of the views, that is the first k views for a random k, keeps it at about 98 percent from one to six views, with no loss at six views and stable results across three seeds.

## Slide 15: Counterfeit Screening: Evaluation on Unseen Prints
Chart: Accuracy on counterfeit prints never seen in training (6 views, 3 seeds)
| Frozen ResNet-50 | Prefix network | Fine-tuned ResNet-50 | Prefix + watermark
6 views | 83.8 | 89.3 | 94.4 | 95
95.0%
on counterfeit prints never seen in training, with the watermark check
Why a stricter split: 279 of 322 readable 500 Taka counterfeits share one serial number, so the usual split tests copies of known prints.
Data: [9] JaalTaka; serial-number audit and print-disjoint split are ours. Earlier Taka counterfeit work: [6] SVM on security features; [7] CNNs; [8] UV flecks + RPN.
Notes: Most counterfeit notes in JaalTaka are copies of a few prints, so the usual test measures recognition of known reprints; a serial-number lookup alone scores 90.2 percent. On truly unseen prints our network drops to about 89 percent; adding the watermark check brings it to 95 percent.

## Slide 16: Watermark Verification: DMWR
1. Remove the lamp: Q = I / (G∗I)
2. Genuine portrait: T = median of Q over genuine notes
3. Residual R = Q − T → two small CNN streams → "watermark clear?"
91.5%
on unseen counterfeit prints (3 seeds, ±0.3)
46× smaller
than MobileNetV2 [22] (47,818 parameters, 0.21 MB), and as accurate: 92.9%, p ≥ 0.375
Baseline [22] Sandler et al., MobileNetV2, CVPR 2018; data [9] JaalTaka. DMWR (denomination-matched watermark residual) is our method.
Notes: Our watermark method divides the back-lit photo by a blurred copy to remove the lamp, subtracts a genuine portrait of the note value and classifies the residual with two tiny networks. With under fifty thousand parameters it reaches 91.5 percent on unseen prints, statistically level with a MobileNetV2 46 times larger.

## Slide 17: Safe Verdict Policy
Note captured
Score above the safe threshold?
"Likely genuine"
"Check by hand" + guided watermark check
yes
no
0 / 88
test counterfeits passed as "likely genuine"
"Likely genuine": the score is higher than every counterfeit seen in validation (57.5% of genuine notes).
"Check by hand": the glass is not sure. It never means "counterfeit".
A screening aid, not a guaranteed counterfeit detector
Test notes: [9] JaalTaka.
Notes: Because a blind user cannot verify the answer, the glass never says a note is counterfeit. It says likely genuine only above a threshold set from validation counterfeits; otherwise it asks for a check by hand. The threshold is the highest score of any validation counterfeit, so a new counterfeit passes with probability about 1 in n plus 1, roughly 1.1 percent. No test counterfeit passed, and 57.5 percent of genuine notes are confirmed from close-up views.

## Slide 18: UV Security-Fibre Verification
85.6%
of 111 real UV photos of genuine notes accepted
88.6%
of SIMULATED fibre-free sheets rejected (not real counterfeits)
The glass's lamp emits 360-395 nm, covering the 365 nm used for banknote checks; banknote paper stays dark while its fibres glow [23]. Prior Taka UV work: [8] (96.3%). Fibre check and photos are ours.
Prototype, off by default
The rejection result is simulated; it must be validated on real counterfeit notes
Notes: Under a UV lamp, genuine 200, 500 and 1000 Taka notes show glowing security fibres. Our check removes the lamp's own blue light and counts thin glowing marks. It accepts 85.6 percent of real genuine photos and rejects 88.6 percent of simulated fibre-free sheets. It stays off by default until real counterfeits are tested.

## Slide 19: Bangla and English Text Recognition
Rendered text (clean)
Chart: 
| All scripts
Before | 9.3
Now | 2.3
Real word photos (hard)
Chart: 
| Bangla | Latin
Before | 39.2 | 62.5
Now | 28.7 | 50.6
Character error rate, lower is better. Measured on evaluation datasets, not yet through the glass.
What helped
Reading the main text block only
Tuned detector and clean-up
Recogniser fine-tuned on real words
What did not
Binarisation, Tesseract, TrOCR, PaddleOCR, dictionaries
Engine [15] EasyOCR with [14] CRAFT; real words from [24] ICDAR 2019 MLT (1,000 test words). Every choice made on validation data.
Notes: On our rendered Bangla and English benchmark the error fell from 9.3 to 2.3 percent. Real street words are much harder: a recogniser fine-tuned on real words and blended with the original weights lowered the error from 39.2 to 28.7 percent for Bangla and from 62.5 to 50.6 percent for Latin script. What helped: reading only the main block of text, tuned detector settings with CLAHE and clean-up rules, and the recogniser fine-tuned on real words and blended fifty-fifty with the original weights. Binarisation, multi-scale reading, Tesseract, TrOCR, PaddleOCR, dictionaries, smaller pictures and a rotation retry did not help.

## Slide 20: Voice Interaction
Speaking
Natural Piper voice, Bangla and English [17, 19]
No broken sound when the Pi is busy
"পড়ছি" (reading) while text is captured
Command results: synthetic voices on a laptop, not human trials on the glasses
Chart: "Glass, …" commands, 12 unseen synthetic voices
| Clean | Whispered | Street noise 0 dB | People talking 10 dB
Commands carried out | 100 | 98.9 | 82.5 | 54.3
212 → 13
false commands in 5,040 ordinary sentences, thanks to the wake word
0.86 s
from the end of speech to the action (median)
Recogniser [11] Vosk; noise from [25] Piczak, ESC-50; voices [17, 19]. Results: paper_evidence/VOICE_COMMANDS_FAST.md.
Notes: The glass now speaks with a natural Piper voice, with eSpeak NG as a fallback, and each sentence is rendered before it plays, which fixed the broken sound on the Pi; a short word and a soft tick tell the user that a long capture is running. These command results come from synthetic voices on a laptop, not from people wearing the glass. Commands start with the word glass. On twelve unseen synthetic voices, clean commands are always carried out, whispered ones 98.9 percent, with street noise as loud as the voice 82.5 percent, and with people talking nearby about half. The wake word cut false commands from 212 to 13.

## Slide 21: Performance on the Raspberry Pi 5
399 ms
currency check, end to end
64 ms
watermark check
562 ms
object scan (YOLOv8s)
680 ms
emotion, face in view
18.3 s
3-line sign, text found once
1.48 GB
peak memory, 30-minute run
Key finding: heat
88.7 °C
peak temperature; the Pi throttled in 76% of samples (idle 71 °C)
Response: a thermal governor slows background scans when hot; better cooling is future work.
Measured on a Raspberry Pi 5 (8 GB) on 13 October 2026, board at its temperature limit; memory from the 1 October run. Changes after 13 October are not yet timed on the Pi.
Board: [12] Raspberry Pi 5 (8 GB). All timings are ours (benchmark_report/, 1 and 13 October 2026).
Notes: Measured on the Raspberry Pi 5 itself. The currency check takes 0.4 seconds, the watermark check 64 milliseconds. Text reading is the slow part at about 18 seconds for a short sign. The board was hot in this run, so we added a thermal governor; the newest changes still need to be timed on the Pi.

## Slide 22: Prototype Testing and Project Status
Prototype version 2 in a staged shop exchange by team members; illustration only, no error rate counted.
DONE
Engineering checks
Each part tested on held-out data, on a laptop and the Pi 5
PRELIMINARY
First field test
Glass camera: currency unreliable, Bangla text not read
IN PROGRESS
Participant trials
Sessions with a visually impaired participant have started
NONE YET
Full user study
No results about users are claimed
Notes: The second prototype on team members. The first field test with the glass camera was not good enough: currency was unreliable and Bangla text was not read, probably because of the low-resolution fixed-focus camera. Sessions with a visually impaired participant have started, with a Bangla voice questionnaire, but no user study is complete yet, so we make no claims about users.

## Slide 23: Future Directions
1
Camera
Higher resolution or autofocus
2
User study
8–12 participants, including their own voice commands
3
More banknotes
Unseen counterfeit prints; UV check on real fakes
4
Speed and cooling
Time the new code on the Pi; better cooling; battery
Done: engineering tests In progress: participant trials Future: the four steps above
Notes: Our roadmap has four steps. First, a better glass camera with higher resolution or autofocus, and a test set taken through the glass. Second, the user study with eight to twelve participants: task time, accuracy, SUS and NASA-TLX, including voice commands spoken by people and Bangla command words. Third, more banknotes: about a hundred unseen counterfeit prints with a bank or the police, and the UV check on real counterfeits. Fourth, speed and cooling: timing the new code on the Pi, better cooling and battery life.

## Slide 24: Conclusion
Built
An offline Raspberry Pi 5 glass that reads Bangla and English, names objects and Taka notes, and speaks Bangla
Investigated
Synthetic training data, prefix training, unseen prints, a safe verdict, DMWR, hand-held notes, OCR, voice
Still to validate
Real counterfeits (also under UV), people's voices, the glass camera, a completed user study
Notes: To sum up: SARA turns three everyday moments, money, reading and the street, into questions the user can ask the glass. It is an assistive glass that speaks Bangla and runs on a Raspberry Pi 5, tested part by part on held-out data, with new methods for counterfeit checking and hand-held notes. Still to be validated: real counterfeit notes, including under the UV lamp; voice commands spoken by people; the glass camera; and a completed user study.

## Slide 25
THANK YOU
Questions?
SARA · Smart Assistive Reading Aid · Independent University, Bangladesh
Notes: Thank you; we are happy to take questions.

## Slide 26: References
[1] World Health Organization. Blindness and vision impairment: fact sheet, updated 10 February 2026.
[2] OrCam Technologies. OrCam MyEye.
[3] Ali A., H. et al. A Google Glass based real-time scene analysis for the visually impaired. IEEE Access 9, 2021.
[4] Brilli, D. D. et al. AIris: an AI-powered wearable assistive device for the visually impaired. arXiv:2405.07606, 2024.
[5] Adusumilli, V. et al. Reading aid and translator with Raspberry Pi for blind people. ICACCS, 2023, pp. 327-331.
[6] Uddin, M. S., Das, P. P., Roney, M. S. A. Image-based approach for the detection of counterfeit banknotes of Bangladesh. ICIEV, 2016.
[7] Pathak, A. et al. Enhanced counterfeit detection of Bangladesh currency through convolutional neural networks. IJIRCST 12(2), 2024.
[8] Chowdhury, A. A. et al. Evaluation of deep learning models on UV ink: a fake money detection scheme with RPN. ICCA (ACM), 2022.
[9] Piyas, B. R. C. et al. JaalTaka: a benchmark dataset for detecting counterfeit Bangladeshi banknotes. Mendeley Data V2, 2025.
[10] Piyas, B. R. C. et al. JaalTaka: a benchmark dataset for detecting counterfeit Bangladeshi banknotes. Data in Brief 64, 112377, 2026.
[11] Alpha Cephei. Vosk offline speech recognition toolkit.
[12] Raspberry Pi Ltd. Raspberry Pi 5 product brief, 2023.
[13] Jocher, G., Qiu, J., Chaurasia, A. Ultralytics YOLO, version 8.0.0, 2023.
[14] Baek, Y. et al. Character region awareness for text detection (CRAFT). CVPR, 2019.
[15] JaidedAI. EasyOCR: ready-to-use OCR with 80+ languages.
[16] Lin, T.-Y. et al. Microsoft COCO: common objects in context. ECCV, 2014.
[17] Rhasspy. Piper: a fast, local neural text-to-speech system.
[18] Li, S., Deng, W., Du, J. Reliable crowdsourcing and deep locality-preserving learning for expression recognition in the wild (RAF-DB). CVPR, 2017.
[19] eSpeak NG text-to-speech.
[20] Nuhash, M. N. I., Akter, S., Mojumdar, M. U. A diverse image dataset for Bangladeshi currency recognition (BanglaTaka). Mendeley Data V1, 2024.
[21] Rafi, M. J. A., Rony, M., Majadi, N. NSTU-BDTAKA: an open dataset for Bangladeshi paper currency detection and recognition. Data in Brief 55, 2024.
[22] Sandler, M. et al. MobileNetV2: inverted residuals and linear bottlenecks. CVPR, 2018.
[23] Mutanen, J., Jaaskelainen, T., Parkkinen, J. P. S. Luminescent security properties of banknotes. IS&T PICS Conference, 2003, pp. 421-424.
[24] Nayef, N. et al. ICDAR2019 robust reading challenge on multi-lingual scene text (RRC-MLT-2019). ICDAR, 2019.
[25] Piczak, K. J. ESC: dataset for environmental sound classification. ACM Multimedia, 2015.
Notes: The sources cited on the slides, numbered as in the slides.

## Slide 27: Resources and Links
Our code and results
SARA: glass software for the Raspberry Pi 5
github.com/aflam330/SARA
Research repository: experiments, results, thesis
github.com/aflam330/Senior_project_wearable_glass_for_blind_people_using_ocr_and_ylo
Datasets
JaalTaka (counterfeit notes)
data.mendeley.com/datasets/2m7wk5cy4c/2
BanglaTaka (note photos)
data.mendeley.com/datasets/3cv2sypkkh/1
NSTU-BDTAKA (hand-held notes)
www.sciencedirect.com/science/article/pii/S2352340924006681
Microsoft COCO
cocodataset.org
ICDAR 2019 MLT
rrc.cvc.uab.es/?ch=15
ESC-50 environmental sounds
github.com/karolpiczak/ESC-50
Open-source tools
Ultralytics YOLOv8
github.com/ultralytics/ultralytics
EasyOCR
github.com/JaidedAI/EasyOCR
Piper text-to-speech
github.com/rhasspy/piper
Vosk speech recognition
alphacephei.com/vosk/
eSpeak NG
github.com/espeak-ng/espeak-ng
WHO vision fact sheet
www.who.int/news-room/fact-sheets/detail/blindness-and-visual-impairment
Notes: Our code is public on GitHub: the glass software and the research repository with every experiment. The datasets and open-source tools we used are linked here.